## Slide 1: PCAPs
http://packetbomb.com/sf18asia

## Slide 2: Solving Real Problems for Real People
Step-by-step case studies

## Slide 3: Packet A-(nalysis) Team
Helping strangers on the Internet via
packetbomb.com

## Slide 4: Slow Tput for first 6.5 Sec
Post on /r/networking
Rack of 7 Dell PowerEdge servers
1Gbps TOR switch
Low throughput
Initial delay of 6.5sec
Troubleshooting for over a month
Show me the pcap

## Slide 5: 6.5 Sec Delay Takeaway
Capture the 3way handshake
  MSS tells you the MTU
  Need wscale to calculate receive window
Add TCP seq numbers to columns
Big round numbers mean something- 200, 400, 800
Set a time reference
Learn TCP/IP basics
  PMTUD
  MTU probing - /proc/sys/net/ipv4/tcp_mtu_probing

## Slide 6: Slow FTP Upload
Replaced Fortigate firewall with new Checkpoint
Video team complains of slow upload to London
NetEng team doesn’t deal with many performance issues
~5Mbps now, was ~20Mbps
To the pcaps!

## Slide 7: Slow FTP Upload Takeaway
Always look at RTT
Latency is a huge factor for some apps/protocols
PSH bit can be an indicator of buffer size
Bytes in flight should reach at least BDP

## Slide 8: DC2DC Transfer Performance
Poor TCP performance between two DCs in one direction
Easily reproducible with FTP or iperf
Problem doesn’t exist in the opposite direction
To the pcaps!

## Slide 9: DC2DC Perf Takeaway
Tcptrace stream graph is your friend
Look at the angle of the line in the stream graph
Changes in angle means something happened
Do sequence number analysis
  Go slow and be patient
  Double and triple check
Get captures from both ends

## Slide 10: Contact
Fill out the session survey!
kary@packetbomb.com
@packetbomb
Packetbomb.com