## Slide 1: Writing a Wireshark Dissector
3 Ways to Eat Bytes

## Slide 2
Introduction
Software Developer with Trihedral UK Limited
  Use C++ and scripting for SCADA toolkit VTScada™
  Use Wireshark with industrial tele-control protocols
Wireshark Core Developer
  First contributed to Wireshark in 1999
  Maintain DNP3 dissector, Windows Build systems, CMake build
  Frequent contributor to “Ask Wireshark”
    Mostly fixing formatting and converting “answers” to comments 

## Slide 3
Topics to be Covered
Wireshark internals brief overview
  Where dissectors fit in
Dissectors
  Brief overview
  Paths to implementation
  Complexity and performance tradeoffs

## Slide 4
Wireshark Internals
Wireshark provides a framework for loading, dissection and visualization of network traffic
Wireshark framework allows individual dissectors access to network data via libwiretap
Wireshark framework provides utility functions for dissectors when dissecting data
Wireshark framework allows dissectors to write out products of dissection

## Slide 5
Dissectors overview
Dissectors “register” their interest in data from a lower level protocol dissector, e.g. tcp port 54321
The lower level dissector hands the payload body to the registered dissector
Dissectors “pick apart” a protocol into the individual elements of the protocol message
Each element of a protocol may have a type, e.g. integer, string, bit field, timestamp
Dissectors provide elements that may be used in display filters

## Slide 6
Dissector output
Set the protocol column
Set the info column
Create tree entries as required
  Create subtree entries for protocol components
  Add values, text to tree entries
Call sub-dissectors as required

## Slide 7
Dissector Construction Options
Text based
  Built-in, with compilation – ASN.1, IDL
  External, without compilation – Wireshark Generic Dissector (WSGD)*
Scripting language based
  Built-in: Lua*
C based*
  Traditional format, requires a development environment

## Slide 8
Demonstration protocol
Made up for this presentation
Has a header with a byte indicating the message type, and a short (2 bytes in big-endian format) for the total message length (including the header)
Commands are:
  connect (20) and connect_ack (21) that have a long (4 bytes in little-endian format) id
  disconnect (60) and disconnect_ack (61) that have a long (4 bytes in little-endian format) id
  request_data and request_reply that have a byte indicating the data type and for the reply an actual data value;
    Data type 0 – a little-endian short
    Data type 1 – a little-endian long
    Data type 2 – a 15 character string

## Slide 9
Text based Dissectors
Protocol definition held in text file(s) in human readable form
Definitions are interpreted or compiled to produce a dissector
Low barrier to entry, although ASN.1 and IDL require a development environment to compile resulting dissector
Interpreted text files are slowest at dissecting packets
Least flexible option for access to libwireshark infrastructure

## Slide 10
Wireshark Generic Dissector (WSGD)
A Wireshark add-on created by Olivier Aveline, info at http://wsgd.free.fr/
Allows dissection of a protocol based on a text description of the protocol elements
Available for Windows and Linux as a plug-in module
Has some limitations but relatively simple to use and doesn’t require a development environment

## Slide 11
WSGD Dissectors
Copy the appropriate version of the plugin into your Wireshark installation:
  Global plugins
  Personal plugins
Copy (or create) the definition files in the required location:
  As specified by the environment variable “WIRESHARK_GENERIC_DISSECTOR_DIR”
  Profiles directory
  User data directory
  Global plugin directory
  Wireshark main directory

## Slide 12
WSGD Basics – Protocol Definition
WSGD requires a protocol definition file, this describes the top-level details of the protocol to be dissected, such as the name.
See file sf18.wsgd

## Slide 13
WSGD Basics – Field Definitions
WSGD requires a field definition file, this describes the fields to be dissected, their names, types and possible values.
See file sf18.fdesc

## Slide 14
Scripting language based dissectors
Protocol definition held in text file(s) using the script language syntax
Definitions are interpreted by the scripting language run-time
Scripting run-time exposes access to libwireshark infrastructure
Not all libwireshark infrastructure exposed
No development environment required
Faster than text dissectors, slower than C

## Slide 15
Lua dissectors
Lua is built-in to Wireshark (on most platforms)
The lua support can be used to build dissectors, post-dissectors and taps
init.lua in the global configuration directory is run at Wireshark start-up
If disable_lua is not set to 0 runs init.lua from the personal configuration directory
Loads all lua scripts (*.lua) in the global and personal plugins directory
Runs any scripts passed on the command line with –X lua_script:xxx.lua

## Slide 16
Lua dissector – Code
See the file sf18.lua

## Slide 17
C based dissectors
Protocol definition, implied in dissector source
Dissector source file compiled into libwireshark or as a plugin
All libwireshark infrastructure available
High knowledge barrier to initial implementation
Full development environment required
Use existing dissectors as a guide
Developers Guide is essential reading, also README.developer

## Slide 18
Place source file in epan\dissectors
Add entry for source to Makefile.common, epan\CMakeLists.txt
Rebuild Wireshark in the normal way
C dissector installation

## Slide 19
C dissector – code
See the file packet-sf18.c

## Slide 20
Comparison of dissectors
For this simple “protocol”, Wireshark displays are almost identical
WSGD and Lua dissectors are quick and easy to develop; edit file and restart Wireshark
WSGD facilities are most limited option, Lua more advanced
C dissectors easy to distribute, build an installer package, easy to contribute back to Wireshark
WSGD 124 lines, Lua 89 lines, C 270 lines

## Slide 21
Comparison of dissector performance
No visible difference for a small capture file, 11 packets
Big capture file (~ 1M packets) load time results:
  WSGD: 1:42.1 – 9.1 x slower than C
  Lua: 0:27.0 – 2.4 slower than C
  C: 0:11.2

## Slide 22
Questions?
Other dissector options?
Future directions?