## Slide 1: SACK / D-SACK How to analyze SACK and D-SACK within Wireshark
Christian Reusch
CRnetPACKETS

## Slide 2: Hello!
I am Christian Reusch
I am here because I love to give presentations.
You can find me at:
Twitter: @crnetpackets
Blog: www.crnetpackets.com
YouTube: CRnetPACKETS
new

## Slide 3: Agenda
SACK
D-SACK
Wireshark SACK Profile
Graphical analysis (TCPtrace)
Profile: https://crnetpackets.com
Tracefile: https://syn-b.it/sf20v
Thanks to Sake Blok for providing the trace

## Slide 4: (D-)SACK RFC Overview
RFC 2018 SACK
RFC 2883 D-SACK
(RFC 6675 SACK based Loss recovery)

## Slide 5: SACK
Introduction

## Slide 6: SACK
Sequence (SEQ)
Cumulative ACK (ACK)
1st SACK Block (LE1 – RE1)
2nd SACK Block (LE2 – RE2)
3rd SACK Block (LE3 – RE3)
4th SACK Block (LE4 – RE4)
    4th Block only w/o TCP timestamp

## Slide 7: SACK Case1
Sender
Seq NxtSeq
4000 5000
5000 6000
6000 7000
7000 8000
ACK sent by Receiver
ACK LE1 RE1
(lost)
4000 5000 6000
4000 5000 7000
4000 5000 8000

## Slide 8: SACK Case2
Sender
Seq NxtSeq
3000 4000
4000 5000
5000 6000
6000 7000
7000 8000
8000 9000
5000 6000
3000 4000
ACK sent by Receiver
ACK LE1 RE1 LE2 RE2 LE3 RE3
(lost)
3000 4000 5000
(lost)
3000 6000 7000 4000 5000
(lost)
3000 8000 9000 6000 7000 4000 5000
3000 4000 7000 8000 9000
7000 8000 9000

## Slide 9: SACK-Facts
SACK negotiated in 3 Way Handshake
1st SACK holds the triggering blocks
  SACK blocks 2-4 should repeat the most recently reported blocks
LE and RE represents a continuous block of bytes that were received

## Slide 10: SACK Facts
Data receiver
  “SACKed” segments could be discarded
  Send SACK immediately
  Use as many SACK block as possible
  In all ACKs which not ACK the highest received byte

## Slide 11: SACK Facts
Data sender:
  “SACKed” packets skipped for fast retransmits
  If retransmission timeout for a segment is reached it MUST be retransmitted in any case, if it is not ACKed so far ( RFC 2018 )

## Slide 12: D-SACK
Introduction

## Slide 13: D-SACK
Sender
Seq NxtSeq
3000 4000
4000 5000
3000 4000
ACK sent by Receiver
ACK LE1 RE1 LE2 RE2 LE3 RE3
4000, ACK lost in transit
5000, ACK lost in transit
5000 3000 4000
Received
Seq NxtSeq
3000 4000
4000 5000
3000 4000

## Slide 14: D-SACK and SACK
Sender
Seq NxtSeq
3000 4000
4000 5000
5000 6000
6000 7000
3000 4000
ACK sent by Receiver
ACK LE1 RE1 LE2 RE2 LE3 RE3
4000, ACK lost in transit
5000, ACK lost in transit
5000 6000 7000
5000 3000 4000 6000 7000
Received
Seq NxtSeq
3000 4000
4000 5000
lost
6000 7000
3000 4000

## Slide 15: D-SACK of SACK
Sender
Seq NxtSeq
1000 2000
2000 3000
3000 4000
4000 5000
5000 6000
7000 8000
2000 3000
3000 4000
ACK sent by Receiver
ACK LE1 RE1 LE2 RE2 LE3 RE3
2000
2000 7000 8000
2000 3000 4000 7000 8000
2000 5000 6000 3000 4000 7000 8000
2000 3000 4000 3000 4000 7000 8000
Received
Seq NxtSeq
1000 2000
dropped
delayed
dropped
delayed
7000 8000
3000 4000
5000 6000
dropped
3000 4000

## Slide 16: D-SACK Facts
D-SACK is always reported in the first SACK block
  First block left edge smaller ACK
  Or subsegment of 2nd block
D-SACK can hold additional SACK blocks
D-SACK advertises I received data twice

## Slide 17: Issue #17315
The DSACK field in Wireshark (< v3.4.7 rc04) works not as expected
  1st SACK block is always identified as D-SACK, wrongly
  But it could be used to filter the 1st SACK block
Solved since Wireshark 3.4.7 rc04
Presentation uses fixed issue (> v3.4.7 rc04)

## Slide 18: Wireshark
It´s time to have a look at the trace:
sf20v-sacked.pcapng

## Slide 19: Takeaways
What have I learned

## Slide 20: Takeaway
SACK first block indicates changes
D-SACK first and (second block)
Non “ACKed” packets maybe discarded
Column occurrence and color rules
D-SACK field coming up with v3.4.7 rc04
tcptrace

## Slide 21: Q & A

## Slide 22: Thank you
I am happy to receive your feedback!
https://forms.gle/GGRAzkJcEuDkx5r36
You can find me at:
Twitter: @crnetpackets
Blog: www.crnetpackets.com
YouTube: CRnetPACKETS