## Slide 1
Successful Ways to use NetFlow and IP SLA
Wednesday June 17th 10:45am – 12:15pm
Presenter Name
Michael Patterson – Product Manager
Michael Krygeris - Software Developer
SHARKFEST '09
Stanford University
June 15-18, 2009
Notes: <number>

## Slide 2: NetFlow
Michael Patterson
Product Manager – Scrutinizer.com

## Slide 3: What is NetFlow
NetFlow is a network protocol developed by Cisco to run on IOS equipment. It collects IP traffic information less the detail of a packet analyzer.
The Router / Switch aggregates traffic into flows and sends up to 30 of them in a single NetFlow packet. A single NetFlow v5 packet can represent thousands of IP Frames from up to 30 hosts.

## Slide 4: Applications for NetFlow
Accounting
Usage-based network billing
Network planning
Security
Denial of Service monitoring
Network monitoring
http://www.cisco.com/en/US/products/ps6601/products_ios_protocol_group_home.html

## Slide 5: NetFlow Complements WireShark
NetFlow Reporting provides details on:
  Top Applications, Hosts, Autonomous Systems, Subnets (i.e. IP Groups), Types of Service, etc.
WireShark Reporting provides packet level details on everything that went over the wire. The problem is that a distributed solution can be expensive.

## Slide 6
Distributed Analysis
Routers, switches & servers can all send flows
The flows are streamed back to Collector
Collector
Mirrored
Port
WireShark
Notes: <number>

## Slide 7
Collector
Notes: <number>

## Slide 8: Distributed Analysis
NetFlow allows most customers to leverage existing routers
90% of the benefits of a packet analyzers without deploying more computers
2% - 3% load on CPU of equipment
Increases network traffic by 1% - 3% of existing traffic load

## Slide 9: Enabling NetFlow & sFlow
NetFlow
Cisco
Enterasys
Adtran
Riverbed
Juniper
3Com
sFlow
Force10
Enterasys
Extreme
HP
Foundry
http://www.plixer.com/products/scrutinizer_activate-netflow.php

## Slide 10: NetFlow v9 Ingress Vs. Egress
NetFlow v9 Ingress is collected on traffic going into (i.e. inBound) an interface. This is how NetFlow v5 collects data. To figure out outBound traffic volume, ingress must be collected on all interfaces and the reporting software then displays outbound traffic. What goes in must go out, right?
NetFlow v9 Egress is collected on traffic going out (i.e. outBound) of an interface. Generally, it is used in combination with Ingress, but it doesn’t have to be.
Why collect with egress? Hardware such as WAN optimizers compress data. Traffic compression with Cisco NetFlow means that what comes in 100 bytes might go out as 50 bytes. If only using ingress flows, the NetFlow reporting software will show 100 bytes outbound, even if it was compressed to 50 bytes. This is because it was calculated using ingress flows.
http://www.plixer.com/blog/scrutinizer/netflow-version-9-egress-vs-ingress/

## Slide 11: Egress Vs. Ingress
http://www.plixer.com/blog/scrutinizer/netflow-version-9-egress-vs-ingress/

## Slide 12: WireShark needs a NetFlow v9 Template
http://www.plixer.com/blog/general/wireshark-needs-templates-to-decipher-netflow-v9/

## Slide 13: Top N Reports
Top Hosts, Applications, ToS, Autonomous Systems, IP Groups, subnets, etc.
Demonstration
http://www.plixer.com/products/free-netflow.php

## Slide 14: ToS: DiffServ

## Slide 15: CBQoS
Blog: http://www.plixer.com/blog/denika/using-cbqos-to-monitor-qos-on-your-network/
Ingress Flow
Egress Flow
Confirm whether CBQoS configurations on the Cisco router are working as planned.

## Slide 16: Network Behavior Analysis

## Slide 17: NetFlow Wrap Up
WireShark provides the details when you need to dig in and see everything
NetFlow Reporting provides the high level details admins need 90% of the time
NetFlow (sFlow) can easily be widely collected

## Slide 18: IP SLA
Michael Krygeris
Software Developer – plixer.com

## Slide 19: What is IP SLA
Cisco IOS IP Service Level Agreements (SLAs) enables customers to perform service level monitoring by measuring both end-to-end latency, packet loss, etc. at the IP layer.
With Cisco IOS IP SLAs, users can verify service guarantees, increase network reliability by validating network performance and proactively identify network issues.
Cisco IOS IP SLAs use active monitoring to generate traffic in a continuous, reliable, and predictable manner, thus enabling the measurement of network performance and health.
http://www.cisco.com/en/US/products/ps6602/products_ios_protocol_group_home.html

## Slide 20: Applications for IP SLA
IP SLA: Jitter
IP SLA: ICMP Echo Configuration
IP SLA: TCP Connect Configuration
IP SLA: HTTP IP Configuration
Others:
  MOS (Mean Opinion Score)
    Involves setting up the correct VoIP codec for your PBX
    A MOS = 5 is not realistic
    Requires a Jitter Probe
  DNS lookup
http://www.plixer.com/blog/general/plixer-and-cisco-ip-sla-jitter-part-1-of-4/

## Slide 21: IP SLA : HTTP IP Configuration
The results of an HTTP operation can be useful in monitoring your web server performance levels by determining the RTT taken to retrieve a web page. The HTTP operation measures the round-trip time (RTT) between a Cisco device and an HTTP server to retrieve a web page. The HTTP server response time measurements consist of three types:
  DNS Lookup—RTT taken to perform domain name lookup.
  TCP Connect—RTT taken to perform a HTTP TCP connection.
HTTP Transaction Time—RTT taken to send a request and get a response from the HTTP serverThe operation retrieves only the home HTML page.
White Paper: http://www.plixer.com/support/wp_request.php?w4=Yes

## Slide 22: IP SLA : HTTP IP Configuration
Router# show ip sla monitor configuration
Router# config t
Router (config)# ip sla monitor <1-2147483647>
Router(config-sla-monitor-http)# type http operation get url <url>
Router(config-sla-monitor-http)# tag <Description of this IP SLA Operation>
Router(config-sla-monitor-http)# frequency <1-604800>
Router (config-sla-monitor-http)# owner <person or group>
Router (config-sla-monitor-http)# tos <0-255>
Router(config-sla-monitor-http)# exit
Router(config)# ip sla monitor schedule <1-2147483647> start-time now life forever
Router# show ip sla monitor configuration statistics <1-2147483647>
Router# show ip sla monitor configuration <1-2147483647>
Router (config)# no ip sla monitor <1-2147483647>
White Paper: http://www.plixer.com/support/wp_request.php?w4=Yes

## Slide 23: IP SLA : HTTP IP Configuration

## Slide 24: IP SLA : ICMP Echo Configuration
The ICMP Echo operation measures end-to-end response time between a Cisco router and any device with an IP Address.
The response time is computed by measuring the time taken between sending an ICMP Echo request and receiving the Echo reply.
ICMP Echo response times can be measured between Cisco routers by enabling the IP SLA Responder.
Using another Cisco router is not required.
White Paper: http://www.plixer.com/support/wp_request.php?w6=Yes

## Slide 25: IP SLA : ICMP Echo Configuration
Router (config)# ip sla monitor responder
Router (config)# exit
Router# show ip sla monitor responder
Router# show ip sla monitor configuration
Router (config)# ip sla monitor <1-2147483647>
Router(config-sla-monitor)# type echo protocol ipicmpecho <ip address or Hostname>
Router(config-sla-monitor-echo)# tag <Description of this IP SLA Operation>
Router(config-sla-monitor-echo)# frequency <1-604800>
Router(config-sla-monitor-echo)#owner <Name of person or group>
Router (config-sla-monitor-echo)# tos <0-255>
Router(config-sla-monitor-echo)# exit
Router(config)# ip sla monitor schedule <1-2147483647> start-time now life forever
Router# show ip sla monitor configuration statistics <1-2147483647>
Router#show ip sla monitor configuration <1-2147483647>
Router (config)# no ip sla monitor <1-2147483647>
White Paper: http://www.plixer.com/support/wp_request.php?w6=Yes

## Slide 26: IP SLA : ICMP Echo Configuration

## Slide 27: IP SLA : TCP Connect Configuration
The IP SLA TCP Connect operation measures the response time taken to perform a TCP Connect operation between a Cisco router and devices using IP. TCP is a transport layer (Layer 4) internet protocol that provides reliable full-duplex data transmission.
The destination device can be any device using IP.
TCP Connect response times can be measured between Cisco routers by enabling the IP SLA Responder.
Using another Cisco router is not required.
White Paper: http://www.plixer.com/support/wp_request.php?w5=Yes

## Slide 28: IP SLA : TCP Connect Configuration
Router (config)# ip sla monitor responder
Router (config)# ip sla monitor responder type <type> ipaddress <ip address> port <1-65535>
Router (config)# ip sla monitor responder
Router (config)# ip sla monitor responder type <type> ipaddress <ip address> port <1-65535>
Router (config)# exit
Router# show ip sla monitor responder
Router# show ip sla monitor configuration
Router (config)# ip sla monitor < 1-2147483647 >
Router(config-sla-monitor)# type tcpconnect dest-ipaddr <ip address or Hostname> dest-port <1-65535>
See Next Slide …
White Paper: http://www.plixer.com/support/wp_request.php?w5=Yes

## Slide 29: IP SLA : TCP Connect Configuration
… Continued
Router (config-sla-monitor-tcp)# tag <description of IP SLA Monitor>
Router(config-sla-monitor-tcp)# frequency <1-604800>
Router (config-sla-monitor-jitter)# owner <person or group>
Router (config-sla-monitor-tcp)# tos <0-255>
Router(config-sla-monitor-tcp)# exit
Router (config)# ip sla monitor schedule <1-2147483647> start-time now life forever
Router# show ip sla monitor configuration statistics <1-2147483647>
Router#show ip sla monitor configuration <1-2147483647>
Router (config)# no ip sla monitor <1-2147483647>
White Paper: http://www.plixer.com/support/wp_request.php?w5=Yes

## Slide 30: IP SLA : TCP Connect Configuration

## Slide 31: IP SLA : Jitter Configuration
The IP SLA UDP jitter operation was primarily designed to diagnose network suitability for real-time traffic applications such as voice over IP (VoIP), video over IP, or real-time conferencing.
Jitter means inter-packet delay variance. When multiple packets are sent consecutively from source to destination, (for example, 10 ms apart) and the network is behaving ideally, the destination should be receiving them 10 ms apart.
If there are delays in the network (like queuing, arriving through alternate routes, and so on) the arrival delay between packets may be greater or less than 10 ms.
Latency, Packet Loss, MOS
White Paper: http://www.plixer.com/support/wp_request.php?w7=Yes
Notes: Using this example, a positive jitter value indicates that the packets arrived greater than 10 ms apart. If the packets arrive 12 ms apart, then positive jitter is 2 ms; if the packets arrive 8 ms apart, then negative jitter is 2 ms. For delay-sensitive networks like VoIP, positive jitter values are undesirable, and a jitter value of 0 is ideal.
<number>

## Slide 32: IP SLA : Jitter Configuration
Router (config)# ip sla monitor responder
Router (config)# exit
Router# show ip sla monitor responder
Router# show ip sla monitor configuration
Router (config)# ip sla monitor <1-2147483647>
Router (config-sla-monitor)# type jitter dest-ipaddr <host name or ip> dest-port <1-65535> codec <codec> advantage-factor <0-20>
Router (config-sla-monitor-jitter)# tag <description of IP SLA Monitor>
Router(config-sla-monitor-jitter)# frequency <1-604800>
Router (config-sla-monitor-jitter)# owner <person or group>
Router (config-sla-monitor-jitter)# tos <0-255>
Router (config-sla-monitor-jitter)# exit
Router (config)# ip sla monitor schedule <1-2147483647> start-time now life forever
Router# show ip sla monitor statistics <1-2147483647>
Router#show ip sla monitor configuration <1-2147483647>
Router (config)# no ip sla monitor <1-2147483647>
White Paper: http://www.plixer.com/support/wp_request.php?w7=Yes

## Slide 33: IP SLA : Jitter Configuration
Notes: Using this example, a positive jitter value indicates that the packets arrived greater than 10 ms apart. If the packets arrive 12 ms apart, then positive jitter is 2 ms; if the packets arrive 8 ms apart, then negative jitter is 2 ms. For delay-sensitive networks like VoIP, positive jitter values are undesirable, and a jitter value of 0 is ideal.
<number>

## Slide 34: Demonstration
Demonstration
Setting up the Cisco Router
Collecting the Data with SNMP
3.99

## Slide 35: IP SLA Complements WireShark
Demonstration

## Slide 36: Using Wireshark to Evaluate SIP/RTP
Notes: <number>

## Slide 37: NetFlow & IP SLA
Utilization via NetFlow
Click for details
MOS via IP SLA
Click for details

## Slide 38: IP SLA Wrap Up
WireShark provides the details when you need graphical packet by packet analysis of transaction latency
SNMP Reporting provides the high level graphical details (e.g. latency trend)
IP SLA like NetFlow allows admins to leverage existing routers as distributed probes.

## Slide 39: Scrutinizer is to NetFlow what WireShark is to Packets
Both are FREE

## Slide 40: More Resources
http://www.cisco.com/en/US/products/ps6601/products_ios_protocol_group_home.html
http://www.plixer.com/support/netflow_v5.html
http://www.cisco.com/en/US/docs/ios/12_4/ip_sla/configuration/guide/hsthresh.html#wp1082249
http://www.plixer.com/products/free-netflow.php
http://www.plixer.com/blog/general/scrutinizer-v70-for-netflow-sflow-analysis/