## Slide 1
BU-11: SPAN/Mirror/Monitor vs. Taps: When should I use what, and why should I care?
Thursday June 18, 2009. 3:15-4:45pm
Betty DuBois
Principal Consultant | DuBois Training & Consulting, LLC
SHARKFEST '09
Stanford University
June 15-18, 2009

## Slide 2: Disclosure
I am opinionated, but do not work for any of the vendors so I get to tell the truth.
I am not a purist.
I am a realist.

## Slide 3: Agenda
Capture Scenarios
  Answer the questions:
    What is it?
    What do I get?
    What don’t I get?
    What will it cost?
Capture from a Switch
Capture from a SPAN/Mirror/Monitor (S/M/M)
Capture from a RSPAN/Remote Mirror
Capture from a Tap
Example scenarios

## Slide 4: Capture from a Switch
What is it?
  Just plug in and go
What do I get?
  Unicast to/from Wireshark host
  Broadcasts & Multicasts for the VLAN the Wireshark host is in
  Bored
What don’t I get?
  Anything else
What will it cost?
  Free
SERIES
A
C
B
D

## Slide 5: Capture from a SPAN/Mirror/Monitor (S/M/M)
What is it?
  S/M/M same concept, name changes depending on the Vendor.
  Copies packets destined to or from a port, group of ports, VLAN or backplane on a switch to the analyzer’s port.
SERIES
X
Y
Z
A
C
B
D

## Slide 6: Capture from a SPAN/Mirror/Monitor (S/M/M)
What do I get?
  The traffic you need to see (maybe)
  Allows you to monitor multiple stations at once.
  If spanning a VLAN, possibly multiple copies of the same packet. (a/k/a why do I have 8 million retransmissions?)
SERIES
X
Y
Z
A
C
B
D

## Slide 7: Capture from a SPAN/Mirror/Monitor (S/M/M)
What don’t I get?
  Valid delta times
    Mixing speeds
    Filtering within the session
    Multiple sessions
    Multiple interfaces within the session
SERIES
X
Y
Z
A
C
B
D

## Slide 8: Capture from a SPAN/Mirror/Monitor (S/M/M)
Why do I care so much about delta times?
  That’s how I make a living
  That’s how I prove whose fault it is
SERIES
X
Y
Z
A
C
B
D
Notes: Cover baseline of the handshake here

## Slide 9: Capture from a SPAN/Mirror/Monitor (S/M/M)
What don’t I get?
  All of the packets you think you are going to
  Packets always in the order they truly happened
  Physically damaged frames
    Might not have been able to bring them into Wireshark anyway due to my NIC driver
SERIES
X
Y
Z
A
C
B
D

## Slide 10: Capture from a SPAN/Mirror/Monitor (S/M/M)
What don’t I get? (continued)
  As many S/M/M sessions as you want or need
    If using redundant links for load balancing, a separate session is needed for each path
  Not all switches have the capability to S/M/M
SERIES
X
Y
Z
A
C
B
D

## Slide 11: Capture from a SPAN/Mirror/Monitor (S/M/M)
What will it cost?
  Time to test during non-production your 1st time
  Time to configure
    Syntax will be different for each vendor/model line/firmware & software versions
  Possible outage
    Memory buffer issue due to session
    Network loop if mis-configured
  Available port on the switch for Wireshark
SERIES
X
Y
Z
A
C
B
D

## Slide 12: Capture from a SPAN/Mirror/Monitor (S/M/M)
Best use case
  S/M/M one interface at a time
  Match speeds
  When you need to just be sure the client commands were received and the responses came back and how fast it happened is unimportant.
SERIES
X
Y
Z
A
C
B
D

## Slide 13: Capture from an RSPAN/ Remote Mirror (R/RM)
What is it?
  Works just like (S/M/M) but it is for a remote switch.
    Could be as close as the same data center rack to as far away as your LAN can take you
  Copies traffic from one interface or VLAN to an analyzer on another switch.
  Traffic is tagged with the RSPAN VLAN id and transmitted via the trunks and the analyzer port is configured as the destination for that RSPAN VLAN
SERIES
X
Y
Z
A
C
B
D

## Slide 14: Capture from an RSPAN/ Remote Mirror (R/RM)
What do I get?
  Key benefit – If a VLAN has hosts across multiple switches, all of that traffic can be sent to a single analyzer
    Of course, then you might get multiple copies of the same packet
  You can create an ACL to filter traffic to the analyzer port
SERIES
X
Y
Z
A
C
B
D

## Slide 15: Capture from an RSPAN/ Remote Mirror (R/RM)
What don’t I get?
  Valid delta times
  Packets in the true order consistently
  All of the packets consistently depending upon load and droppage
SERIES
X
Y
Z
A
C
B
D

## Slide 16: Capture from an RSPAN/ Remote Mirror (R/RM)
What will it cost?
  Have to create an RSPAN VLAN on all switches involved in the path
  All switches in the path must support RSPAN
  Have to allow the RSPAN VLAN on all trunks in the path
  Not all vendors support R/RM
SERIES
X
Y
Z
A
C
B
D
Notes: RSPAN hardware requirements: http://www.cisco.com/en/US/docs/switches/lan/catalyst6500/catos/5.x/configuration/guide/span.html#wp1020144

## Slide 17: Capture from a Tap
To Network
To Analyzer
What is it?
  Full duplex, high speed splitter
SERIES
X
Y
Z
A
C
B
D

## Slide 18: Capture from a Tap
To Network
To Analyzer
What do I get?
  Every packet
  Every packet in the correct order
  Valid delta times
  Ability to capture what you want without having to configure the switch and all the politics involved therein
SERIES
X
Y
Z
A
C
B
D

## Slide 19: Capture from a Tap
To Network
To Analyzer
What don’t I get?
  Both channels in the same trace
    An aggregation tap will take care of that
    If using an aggregation tap, there is a risk of over subscribing
  An entire VLAN at once
SERIES
X
Y
Z
A
C
B
D

## Slide 20: Capture from a Tap
To Network
To Analyzer
What will it cost?
    $$$ for each tap
    If your environment is redundant and load balanced, multiple taps will be required
SERIES
X
Y
Z
A
C
B
D

## Slide 21: Capture from a Tap
To Network
To Analyzer
What will it cost?
    Inserting the tap requires a change control window
      To handle that, taps are inserted and left there. You don’t move them around every 20 minutes. But that is not efficient use of the resource.
      So if you insert it and leave it there forever, isn’t that a single point of failure for my mission critical link? Yes
SERIES
X
Y
Z
A
C
B
D

## Slide 22: Which Should We Use?
Simple network
Users are complaining of slow response time from the server
Notes: Diagram from www.flickr.com/photos/mellertime/262539794/

## Slide 23: Which Should We Use? User Complaint of Slow Web Response
Notes: Diagram from www.edrawsoft.com/Cisco-Network-Design.php

## Slide 24: Which Should We Use?
User complaint:
  Call disconnects
  VoIP phones are off access layer switches
  Call Manager off the distribution switch
Notes: Diagram from http://www.cisco.com/en/US/solutions/ns340/ns414/ns742/ns656/net_design_guidance0900aecd804ab672.pdf

## Slide 25: So What is the Answer?
It depends!
  On your goals
  On your budget
  On your issue
  On your company politics
  On your change control policies

## Slide 26: Bettyland Approach
Use NetFlow and/or sFlow to see the big picture and where the issues are.
Use Wireshark to look at specific issues.
Tap when possible.
SPAN when necessary.
Focus at one issue at a time.
Remember: You can have it all,
but you can’t have it all at once!!

## Slide 27: Questions
??????????????

## Slide 28: Thanks for coming!
Hope you enjoyed Sharkfest 2009