## Slide 1
Writing Your Own Capture Tool With WinPcap & AirPcap
Thursday, June 18th, 2009
Gianluca Varenni
Senior Software Engineer | CACE Technologies, Inc.
gianluca.varenni@cacetech.com
SHARKFEST '09
Stanford University
June 15-18, 2009

## Slide 2: Agenda
WinPcap architecture
A small WinPcap application
  Listing adapters
  Opening an adapter for capture
  Processing and decoding packets
AirPcap-specific features
  Native vs. WinPcap API
  Channel selection
  Packet meta-information

## Slide 3: What’s WinPcap?
Packet capture library for Windows.
Initially a port of tcpdump/libpcap to Windows.
Optimized for packet capture, it supports packet injection.
Support for all the Windows NT versions (from NT4 on, x86 and x64).
Literally thousands of apps based on WinPcap.
  Wireshark
  Nmap
  Snort
  ...

## Slide 4: WinPcap architecture
packet.dll
wpcap.dll
Packet Capture
Driver
(npf.sys)
packets
npf.sys
kernel buffer
network tap
NIC driver
Application
packets
kernel buffer
network tap
NIC driver
Application
packets
user mode
kernel mode
network
kernel mode
network
user mode

## Slide 5: A small WinPcap application
DEMO

## Slide 6: BPF filtering
Berkeley Packet Filter
Ethernet Filter
icmp
(000) ldh [12]
(001) jeq #0x800 jt 2 jf 5
(002) ldb [23]
(003) jeq #0x1 jt 4 jf 5
(004) ret #96
(005) ret #0
802.11 Filter
type data
subtype qos-data
(000) ldb [3]
(001) lsh #8
(002) tax
(003) ldb [2]
(004) or x
(005) tax
(006) ldb [x + 0]
(007) and #0xfc
(008) jeq #0x88 jt 9 jf 10
(009) ret #96
(010) ret #0

## Slide 7: BPF filtering
DEMO

## Slide 8: AirPcap
Bare 802.11 frames + meta-information.
802.11a/b/g/n (depending on the adapter)
Two programming interfaces
  WinPcap API: basic functionalities
  AirPcap API: all the features of AirPcap
  It’s possible to mix and match the two APIs
  Sample airpcap_and_libpcap (_with_filter)

## Slide 9: AirPcap
DEMO

## Slide 10: Channel selection
AirpcapDeviceSetChannel
  Sets the (control) channel on the device.
  Affects all the applications capturing with the device
  Takes the channel number (e.g. 1-14) as parameter
AirpcapDeviceSetChannelEx
  Uses frequencies
  In case of 802.11n, it allows to choose the extension channel.

## Slide 11: Packet meta-information
Delivered with every 802.11 packet.
Out-of-band information
  Channel frequency
  Rate
  Signal/Noise
  RSSI
  Specific 802.11n information
Link layer in use decides which type of meta-information is delivered.
  DLT_IEEE802_11 (No meta-information)
  DLT_PPI (PPI)
  DLT_IEEE802_11_RADIO (Radiotap)
Use AirpcapSetLinkType to set the link layer.

## Slide 12: Questions?

## Slide 13: The WinPcap project
WinPcap = libpcap for Windows
Started in 1999 as a university project
Under the CACE wings since 2005
Team:
  Gianluca Varenni
  Loris Degioanni
  Fulvio Risso
  John Bruno