## Slide 1: How I Learned to Stop Worrying and Love the PCAP
Kary Rogers
Zscaler, GCS Center of Excellence

## Slide 2: Hello!
I am Kary Rogers
I like packets.
You can find me at @PacketBomb
Download files: packetbomb.com/sf21vus

## Slide 3: Wireshark Fundamentals
Do you find Wireshark overwhelming?
Don’t know where to start?
Not sure if you captured the problem?
No idea how to find the problem?
This session is for you

## Slide 4: Download Files
packetbomb.com/sf21vus

## Slide 5: When to Wireshark
Wireshark is a surgical tool
Zoomed in view of a problem
Specific problem description with specific data

## Slide 6: When Not to Wireshark
High level view of network health
Top talkers across the enterprise
Traffic profile across the enterprise
Lots and lots of data
Non-specific problems AKA slow network

## Slide 7: Before Analysis
Defining the Problem
Capturing the Data
Verifying the Data

## Slide 8: Defining the Problem
Problem statement
Push from generic to specific
Validate the problem
Do the investigation now so that it’s easier later

## Slide 9: Narrow the Problem
One application? Multiple?
Slow? Broken? Timeout? Error message?
When did it start?
Every time? Intermittent?
One person? Multiple people?
Exact steps to recreate? Random?

## Slide 10: Before You Get Data
Know the exact nature of the problem
Who it affects
When it started
When it affects them
How it affects them
Across what versions of OS and applications?
What else?

## Slide 11: Defining the Problem Exercise
Reported problem: A new website loads slowly
How can we push this from generic to specific?
Choose the question that will lead you to a more detailed information that you need to narrow down the issue

## Slide 12: Defining the Problem Exercise
Pick the best question:
Is it slow or does it not load at all or only partially?
What’s wrong with it?
Answer: It loads, it’s just slow

## Slide 13: Defining the Problem Exercise
Pick the best question:
Does the whole page load slowly a bit at a time or just a long pause before it loads?
What are your DNS settings?
Answer: There’s a long pause before the page loads. When it does load, it’s fairly quick.

## Slide 14: Defining the Problem Exercise
Pick the best question:
When did the problem start?
How long has the problem been going on?
Answer: This is a new site and it has always done this.

## Slide 15: Defining the Problem Exercise
Pick the best question:
Did you reboot?
Is anyone else seeing the same issue?
Answer: Everyone sees the issue when it happens.

## Slide 16: Defining the Problem Exercise
Pick the best question:
Does it happen every time of just sometimes at random?
Do you notice anything else?
Answer: It happens at random times.

## Slide 17: Defining the Problem Exercise
Based on this narrowing down investigation:
The page loads fast once it loads, but is slow to respond. Server issue? Content filter?
Happens randomly, so could be a network or server event.
Probably on the server end since it’s a new site, is the only one having an issue & affects everyone.

## Slide 18: Capturing the Data
Reproduction plan
Where to capture
How to capture (skipped for time)

## Slide 19: Reproduction Plan
Based on the narrowing the problem
Verify there’s no active application connection between client and server
Start the capture
Then start the application / initiate the connection

## Slide 20: Where to Capture
Close to the source of complaint e.g. user
Near server
Both ends if possible
Make sure system times are in sync

## Slide 21: Verifying the Data
Note the time of the issue
Verify timespan of pcap in Statistics -> Capture File Properties
Wireshark time is relative to the local machine
Filter for client and server IPs
Do you see the SYN?
If you need application data, make sure packets aren’t truncated

## Slide 22: Verifying the Data Exercise
We worked with a user to understand the issue and recently managed to reproduce it ourselves while capturing data on our machine and the server. Now we need to verify the data:
The issue occurred at 10:38pmPT
The client IP is 10.0.100.15
The server IP is 192.168.200.230
Go to “Unit 1 > Lesson 3” and unzip the pcaps

## Slide 23: Verifying the Data Exercise
Does the client capture cover the time of the issue?
Does the server capture cover the time of the issue?
Is there traffic to and from the client and server IPs
Did we capture the beginning of the connection?
Did we get full packet length captures?
The issue occurred at 10:38pmPT
The client IP is 10.0.100.15
The server IP is 192.168.200.230
Go to “Unit 1 > Lesson 3” and unzip the pcaps

## Slide 24: Before Analysis Recap
Defining the problem
  Be specific
Capturing the data
  Close to the source of complaint
Verifying the data
  Start and end of issue correlates with captured data

## Slide 25: Wireshark Setup
Wireshark configuration
Working with profiles
Display filters and coloring

## Slide 26: Wireshark Setup Exercise
Add the HTTP server response time as a column
Add a conversation coloring rule for each conversation between the client and server
Create a saved display filter for HTTP requests and responses
Define a hostname resolution of SlowWebServer for the server IP

## Slide 27: Analysis First Steps
PCAP summary
Conversations
Find the delay

## Slide 28: PCAP Summary Exercise
Open the SlowHTTP-client.pcap and answer:
What is the average pkts/sec for the whole pcap?
What is the average packet size for TCP port 80?
What is the average bytes/sec for IP 192.168.200.230?
What percentage of packets are IPv6?

## Slide 29: Conversations Exercise
Open the SlowHTTP-client.pcap and answer:
How many IPv4 conversations are there?
How may TCP conversations are there?
Which TCP conversation has the most bytes?
Which destination IP is the top receiver in bytes?

## Slide 30: Finding the Delay Exercise
Open the client and server side pcaps:
What is the conversation of the slow web page load?
What is the initial RTT in the client-side capture?
How long does it take for the HTTP response in the client-side capture?
How long does it take for the HTTP response in the server-side capture
Who is responsible for the delay?

## Slide 31: Questions?
kary@packetbomb.com
@Packetbomb
Youtube.com/packetbomb
Fill out your survey!

## Slide 32: Case Study Exercise
packetbomb.com/sf21vus
Click on Case Study