## Slide 1: More Mileage from Your Tools: Problem Isolation with TLS and TCP
George Cragg
Dräger Medical Systems, Inc.
https://github.com/gacragg-github/Sharkfest2023 -or- https://bit.ly/3MNrVSF

## Slide 2: Hello!
I am George Cragg
You can find me at george.cragg@draeger.com / gacragg@gmail.com or on LinkedIn. I am a network engineer/wireless specialist with a medical device company near Boston, MA.
https://github.com/gacragg-github/Sharkfest2023 -or- https://bit.ly/3MNrVSF

## Slide 3: Abstract
As a network tool, Wireshark is often used for diagnosis and to prove/disprove the network contribution to various communication problems that inevitably arise. Here we explore a case study of problem isolation down to a finer level than just 'it's not the network'.
https://github.com/gacragg-github/Sharkfest2023 -or- https://bit.ly/3MNrVSF

## Slide 4: Sea Story Time
Using Our Favorite ToolTM to solve real-world problems
Can we provide more value than just it’s not the network?
Some basic review of TCP and TLS features
Highlight some of the different stakeholders under different scenarios
https://github.com/gacragg-github/Sharkfest2023 -or- https://bit.ly/3MNrVSF

## Slide 5: The case of ‘we added security and now the network is broken’
Process: IoT device is locally controlled by Windows system & sends reports to remote Linux platform
Problem: Once security is enabled, reports are no longer available in database and error is generated (Linux log)
https://github.com/gacragg-github/Sharkfest2023 -or- https://bit.ly/3MNrVSF

## Slide 6: How it works - 1
Local controller model is kiosk-style app

## Slide 7: How it works - 2
“Worked fine before, but when we enable security, the network blocks the traffic”
Q: Do you use TCP or UDP? A: ….
Q: How did you add security? A: TLS

## Slide 8: Players
Three different teams
  Embedded
  Windows
  Linux
What about network?
Usual…

## Slide 9: Even Better
“All I did was add TLS”
“I do a packet-by-packet copy”
“Works fine without security so must be sending me bad data – maybe changed by the network”

## Slide 10: Some things we need
TCP
  Reliable
  Ordered
  Flow control
  Byte stream
No message boundary expressed or implied
TLS
  Confidentiality/Integrity/ Authentication (CIA)
  Works on top of TCP
  Uses Record Protocol to move protected data

## Slide 11: Some things we need
Multiple points of data agglomeration
Reduce overhead for Efficiency by accumulation
Application layer messages
Protected TLS record
TCP segments

## Slide 12: Segmentation Schemes

## Slide 13: Segmentation Schemes

## Slide 14: Segmentation Schemes

## Slide 15: Segmentation Schemes

## Slide 16: TCP PSH Flag
RFC793
Search Google: discussion about usefulness and specific behavior
A sending TCP is allowed to collect data from the sending user and to send that data in segments at its own convenience, until the push function is signaled, then it must send all unsent data. When a receiving TCP sees the PUSH flag, it must not wait for more data from the sending TCP before passing the data to the receiving process.

## Slide 17: TCP PSH Flag
Talk to others to debate true meaning and possible subtleties
Practically I share my experience but defer to experts:
  Either always set when data is present (tcp.len >0)
  Indicates send buffer size of transmitter

## Slide 18: TCP MSS
TCP actors announce the maximum data payload they can receive
Sent with SYN as an option field
Common maximum: 1460
Default: 536
Warning: middle boxes can perform MSS Clamping
Notes: Image from https://www.cloudflare.com/learning/network-layer/what-is-mss/

## Slide 19: TLS Alert
TLS protocol supports mechanism to provide information on errors
RFC5246
  Alert messages convey the severity of the message (warning or fatal) and a description of the alert
Once session established contents are protected i.e. specific details are encrypted
enum {
close_notify(0),
unexpected_message(10),
bad_record_mac(20),
decryption_failed_RESERVED(21),
record_overflow(22),
decompression_failure(30),
handshake_failure(40),
no_certificate_RESERVED(41),
…

## Slide 20: Reverse Engineering
How does process work from my simple point of view?
My means how I think about what is happening in the context of network traffic
Capture

## Slide 21: Reverse Engineering
Approach – observe failure
  Capture on-network traffic (not on-host - why?) at appropriate location – as close to source as possible
  Ask SME to trigger operation, wait a few seconds, then trigger again. Feedback on failure - errors show in the app logs. On success, indicated as such in app logs.
  Can we find it? I rarely use timestamps…
Dataset: 1_ReverseEngineerProfile.pcapng
https://github.com/gacragg-github/Sharkfest2023 -or- https://bit.ly/3MNrVSF

## Slide 22: Reverse Engineering with RFC5246
A.1. Record Layer
struct {
uint8 major;
uint8 minor;
} ProtocolVersion;
ProtocolVersion version = { 3, 3 }; /* TLS v1.2*/
enum {
change_cipher_spec(20), alert(21), handshake(22),
application_data(23), (255)
} ContentType;
struct {
ContentType type;
ProtocolVersion version;
uint16 length;
opaque fragment[TLSPlaintext.length];
} TLSPlaintext;
ContentType | As hex
change_cipher_spec(20) | 0x14
alert(21) | 0x15
handshake(22) | 0x16
application_data(23) | 0x17

## Slide 23: Reverse Engineering
Notes
  IO Graph funnel: all  tcp  tcp.flags.syn == 1
  Packet pane: find port with tcp.flags.syn == 1
  Check flow of that port on IO graph tcp.port == 7777
  No decoder – check bytes with follow stream
    https://www.rfc-editor.org/rfc/rfc5246#page-68
    All start with ContentType, Version
  Set decode as to TLS
    Looks good to me… at least TLSv1.2 in use

## Slide 24: Packet-by-Packet copy
Pray tell… what is this? L3 Routing? Proxy? NAT?
  Dataset: 2_IOT.pcapng
  Dataset: 2a_LocalController.pcapng
Capture
Capture

## Slide 25: Packet-by-Packet copy
Approach – compare packets streams at different points
Model | Possible Differences
L3 | IP Addressing
L3 | TTL
L3 | QoS
L4 | TCP Ephemeral port
L4 | TCP Options
L4 | TCP Segmentation
L4 | TCP Seq No. (absolute)
L7 | TLS Handshake parameters

## Slide 26: Packet-by-Packet copy
Findings
  Not a packet-by-packet copy
  TCP connection is terminated at Local Controller and a new one is formed
  TLS session is pass-thru: end to end protection extends through Local Controller but bytes are re-segmented
  Better model description: byte-by-byte copy (?)
Result
  Nothingburger here – does not behave the way developer thinks it does, but behavior is not faulty in any observed way
  Even if these changes turn out to be root cause, system needs to be able to handle this
    Behavior is within TCP/TLS envelope & compliant to RFCs

## Slide 27: What does good look like?
Remember – I am a one-trick pony
I need to see the operation from the point of view of the communication profile
  where Wireshark comes in
Disable TLS at system level, and let's see a successful run
  Dataset: 3_IOT_noTLS.pcapng
Notes: Pony: Designed by Freepik

## Slide 28: What does good look like?
Approach
  IO Graph
  Follow stream  view as hex dump
    Focus on client to server by selecting direction in the drop down

## Slide 29: What does good look like?
We can export the client data to a file for later use
Why do I want to do that, you ask?
  Because I want to isolate the problem away from the products and provide my own clients/servers under my control to probe behavior
  I don’t know the underlying protocol and really don’t want to
  Follow TCP Stream  (select client:  192.168.0.1:7777)  Show data as Raw  (copy and paste)

## Slide 30: Extract Client Data
Open said file… these are the bytes sent by the client
LF 0x0a or CRLF 0x0d0a added to each segment
  Not part of protocol

## Slide 31: What does failure look like?
Dataset: 2a_LocalController.pcang
Server throws Encrypted Alert, per TLS RFC, to shutdown connection at certain point
  Reproducible – zero variance is always nice!
Conclude
  Server is not happy, but does not mean it is a server problem
  Could be bad client data or whatever
  But gives a clue to what log to go look in – maybe server will tell us what it doesn’t like?

## Slide 32: What is Failure Not?
No evidence of a network issue
If going to the cloud, could have proxy/load balancer/NAT/firewall/TLS decryption … middle boxes … but this is in a lab with none of that
Packets are getting through
  Though changed by Local Controller, still standards compliant
Can we do any more to help besides just point the finger back at software? Let’s get more mileage from the tools.

## Slide 33: Baseball Analogy
Single: Not the network
Double/Second Base: Client or server?
Triple/Third Base: Look here on the problem system
Home Run: change this specific thing and your problem will be gone…
(Walk: you should have known it’s not the network but you make me say it anyway)

## Slide 34: Anomaly Detection
Back to Dataset: 2a_LocalController.pcapng with tcp.len > 0
TLS Record crosses segment boundary and PSH bit is not always set when a complete record exists

## Slide 35: Anomaly Detection

## Slide 36: Anomaly Detection
Encrypted Alert shows up here
Reproducible – we have correlation but don’t know if packet 21 is a trigger, or just represents delay

## Slide 37: Anomaly Detection
“Correlation does not imply causation”
Well known fact

## Slide 38: Anomaly Detection
“Correlation does not imply causation”
Well known fact
“Causation does imply correlation”
Lesser-known fact
Notes: We look for the set of things that correlate, and hope that one of them turns out to have a causal relationship

## Slide 39: Hypothesis Test 1
Server cannot handle PSH bit set for incomplete TLS records
  -- Doubt this has anything to do with our problem
  ++ Easy to test so why not (I need special HW)
Test: clear PSH bit in the client  server data stream of specific incomplete TLS record. Do we get any change in behavior? Looking for any signal: success/failure, change in log message, no log message, etc.
Do I have control? Can I move the needle?

## Slide 40: Packet Mangling
Where?
1/ Source of data, but we know Local Controller changes traffic flow
2/ Probably OK, but must ensure no changes in flow across LAN
3/ Server seems to have the problem and all changes are in effect
Notes: Notice not focused on trigger to report generation? That piece seems to be working – data is generated and a nok log is generated so seems like trigger is ok.

## Slide 41: Packet Mangling
Where?
1/ Source of data, but we know Local Controller changes traffic flow
2/ Probably OK, but must ensure no changes in flow across LAN
3/ Server seems to have the problem and all changes are in effect

## Slide 42: Packet Mangling
Where?
1/ Source of data, but we know Local Controller changes traffic flow
2/ Probably OK, but must ensure no changes in flow across LAN
3/ Server seems to have the problem and all changes are in effect

## Slide 43: Packet Mangling
Where?
1/ Source of data, but we know Local Controller changes traffic flow
2/ Probably OK, but must ensure no changes in flow across LAN
3/ Server seems to have the problem and all changes are in effect

## Slide 44: Packet Mangling
Select TCP traffic
At given frame offset, set bit[s] or byte[s]
Recalculate TCP/IP/Eth checksums
Note the operation

## Slide 45: Packet Mangling

## Slide 46: Hypothesis Test 1
Dataset: 4_LocalCtrlClearPUSH.pcapng
  Review change in PSH bit; no effect on system behavior

## Slide 47: Hypothesis Test 2
Server can’t handle TLS records that cross segment boundary
Approach to test
  Make my own client and vary parameters (MSS, timing) to get TLS records to move within the segments
  Use Python and a lot of Google/Stack Exchange
    Might use ChatGPT today…
  No developer here – don’t play one at work, didn’t sleep at a Holiday Inn Express last night, so a lot of Google
Notes: Wireshark provides a fundamental advantage: know what we expect at the packet level so feedback is fast

## Slide 48: Change Segmentation
Try to do this w/o a product
Why? Because I can’t, not sure development team can in any reasonable time and sometimes we go fishing… not always easy to convince others to spend time and money on a fishing trip

## Slide 49: Change Segmentation
Step 1 – figure out how to make my own client
  -- Don’t know protocol or if we have enough to fake it
  -- No guarantee of success in even running the test
  ++ Lots of Python information on Stack Exchange
  ++ Wireshark exported client-side protocol for us(!)
  ++ Relatively easy to try
https://pypi.org/project/sslpsk/
https://www.geeksforgeeks.org/read-a-file-line-by-line-in-python/
Notes: Line by line even does the EOL characters strip!

## Slide 50: Change Segmentation
Read Wireshark output line by line and strip LF, convert to bin
Adjust timing on a per-line basis  corresponds to per application message from original ‘good’ test
Default timing per message
Send message

## Slide 51: Change Segmentation
Validation: Does test client fail in same way as system?
  Inject bytes into server with no controls in place
Dataset: 5_LocalCtrl_nodly_fail.pcapng
Name of file gives you the hint
  Encrypted Alert moved, but notice timing: MUCH faster now
  Suspect that same failure mode, but sending data faster means relative time of Alert is delayed
  Log files on server indicate same failure mode

## Slide 52: Change Segmentation
Validation: If we replicate timing observed, what happens?
Dataset: 6_LocalCtrl_ReplicateDly_fail.pcapng
  Adjust timing in python: add time.sleep() at specific lines of input to provide better control
  Moved from 3 packets  2, but still fails when this 5th TLS record is split

## Slide 53: Change Segmentation
Hypothesis Test: Force each TLS record as separate segment(s)
Dataset: 7_LocalCtrl_AddDly_ok.pcapng
  Add 10ms per command (which is a line in the exported file from Wireshark)
It works!
Four TLS records no longer share a partial 5th
560byte record is now by itself
5th record is now 1504bytes instead of 1488

## Slide 54: Change Segmentation
We got the needle to move!
  Major success – hypothesis: Server can’t handle mixed partial and complete TLS records in a given segment
  Server software teams says ‘all of this network handling comes from a base class’
    … And we have never seen this problem before…

## Slide 55: Change Segmentation
Hypothesis Test: Force each TLS record as separate segment(s) using MSS clamping instead of timing
  Linux host so straightforward; firewalls can often do it too
  Dataset: 8_LocalCtrl_mssClamp_fail.pcapng
[user@ws]$ sudo ip route add 10.227.1.36/32 via 10.228.1.1 advmss 565 [user@ws]$ netstat -rn Kernel IP routing table Destination Gateway Genmask Flags MSS Window irtt Iface 0.0.0.0 10.228.1.1 0.0.0.0 UG 0 0 0 nic0 169.254.0.0 0.0.0.0 255.255.0.0 U 0 0 0 nic0 10.227.1.36 10.228.1.1 255.255.255.255 UGH 605 0 0 nic0 10.228.0.0 0.0.0.0 255.255.0.0 U 0 0 0 nic0

## Slide 56: Change Segmentation
MSS is 500, so first 560byte TLS record is split
  Server does not like this
  We got more information now – it is not just the 5th split record, if the first record is split it fails
  But… notice from 7_LocalCtrl_AddDly_ok.pcapng, plenty of split records after the first few
  Remember: same base class handling communications (?)

## Slide 57: Change Segmentation
Lets vary MSS until we get a change in behavior
  Dataset: 9_LocalCtrl_mssClamp_increase.pcapng
Useful filter
  (tcp.len > 0) || (tcp.options.mss_val)
  Column callout: tcp.options.mss_val
Conclude: when MSS is sufficient to fully contain 560byte TLS record in this position of protocol, system works. Cannot have a partial record here, either.
  But remember… all handled by same base class
It works!

## Slide 58: Change Segmentation

## Slide 59: Conclusion
Root cause from network POV is isolated to server handling of specific TLS record segmentation
  Why? I have no idea! That is a C++ software developer question…
  Behavior is allowed per RFC, so implementation defect
  Base class so all behavior should be the same is not supported (my interpretation)
Local Controller does not behave the way team thinks it does
  No impact here
We did not find true root cause, but able to point software team to narrow code area and fix generated in less than an hour

## Slide 60: Providing More Value
Packet capture and analysis provides for indication of what and how it may have failed – but not the critical why
Closed-box testing with packet capture as our guide to move the needle helps reduce the problem space leading to faster time to resolution
Hypothesis testing of observable correlation conditions relative to failure guided us to a solution
Wireshark enabled relatively easy protocol replication

## Slide 61: Baseball Analogy
Single: Not the network
Double/Second Base: Client or server?
Triple/Third Base: Look here on the problem system
Home Run: change this specific thing and your problem will be gone…
(Walk: you should have known it’s not the network but you make me say it anyway)

## Slide 62: Baseball Analogy
Single: Not the network
Double/Second Base: Client or server?
Triple/Third Base: Look here on the problem system
Home Run: change this specific thing and your problem will be gone…
(Walk: you should have known it’s not the network but you make me say it anyway)

## Slide 63: Thank you! Please provide feedback per conference guidelines